MIDEM 2025
VACASK –
a novel analog integrated circuit simulator
Árpád Bűrmen
University of Ljubljana
Faculty of Electrical Engineering

---
What is VACASK
- Verilog-A Circuit AnalySis Kernel
- Analog circuit simulator
- Spectre-like input syntax
- Modern C++
- Short (44k lines)
- Easy to extend
- Verilog-A device models
- OpenVAF Verilog-A compiler
  https://github.com/arpadbuermen/OpenVAF
- KLU linear solver
CMOS ring oscillator
load “psp103v4.osdi”
include “cmos_models.inc”
model isrc isource
model vsrc vsource
subckt inv(in out vdd vss)
parameters w=10u l=0.2u fac=2
  mp (out in vdd vdd) pmos w=w*fac l=l
  mn (out in vss vss) nmos w=w l=l
ends
subckt ring()
  x1 (1 2 vdd 0) inv
  x2 (2 3 vdd 0) inv
  x3 (3 1 vdd 0) inv
ends
vdd (vdd 0) vsrc dc=1.2
subckt start()
  ipulse (0 1) isrc type=”pulse” v0=0 v1=1u delay=1n rise=1n fall=1n width=1n
ends
control
  elaborate circuit(“ring”, “start”)
  analysis tran1 tran step=0.05n stop=1u maxstep=0.05n
endc
https://codeberg.org/arpadbuermen/VACASK

---
Features
// ring oscillator definition here ...
control
  elaborate circuit(“ring”, “start”) // with startup pulse
  analysis tran1 tran step=0.05n stop=1u maxstep=0.05n
  elaborate circuit(“ring”) // no startup pulse
  analysis tran2 tran step=0.05n stop=1u maxstep=0.05n
  postprocess(PYTHON , “runme,py”)
endc
embed “runme.py” <<<FILE
  from rawfile import rawread
  import numpy as np
  import matplotlib.pyplot as plt
  fig1, ax1 = plt.subplots(2, 1)
  tran1 = rawread('tran1.raw').get()
  t = tran1["time"]; v1 = tran1["1"]
  fig1.axes[0].set_title('Oscillator startup, without a pulse')
  fig1.axes[0].plot(t*1e6, v1, color="blue", marker=".", label="v(1)")
  tran2 = rawread('tran1.raw').get()
  t = tran2["time"]; v1 = tran2["1"]
  fig1.axes[0].set_title('Oscillator startup, with a pulse')
  fig1.axes[1].plot(t*1e6, v1, color="blue", marker=".", label="v(1)")
  plt.show()
>>> FILE
- Model/analysis separation
- SPICE analyses + HB
- Parameterized, hierarchical
- Sweep anything
- Alter parameters wo. restart
- Change topology wo. restart
- Precise (residual checks)
- Fast (designed for modern CPUs)
- Xschem schematic editor
- IHP OpenPDK (SG13G2 node)

---
OpenVAF Verilog-A compiler
Compilation time in seconds for various Verilog-A models
- Free (GPL V3) Verilog-A compiler.
- Author: Pascal Kuthe
- Revived as OpenVAF-reloaded (2024)
- Can handle all public Compact Model Coalition (CMC) models,
  supports large part of Verilog-A.
- Represents model with a generic system of equations, not limited to SPICE.
- Optimizes equations using
  modern compiler techniques.
- Fast (usually below 1s), LLVM-based,
  generates highly optimized machine code.
- Written in Rust.
	PSPv103	BSIM4	EKV2.6	JUNCAP200	HICUM/L2v3.0
OpenVAF	3.48	6.7	0.23	0.61	0.72
Xyce ADMS	109	25.1	9.6	16.6	22
ADS	33.9	27.0	2.5	5.1	7.7
Spectre	27.4	-	6.1	11.4	19.7
Runtime of HICUM/L2v2p4p0 characteristics simulation
Case	Time [s]	Case	Time [s]
Ngspice (OpenVAF)	9.16	ADS (Verilog-A)	8.63
Ngspice (builtin)	14.64	ADS (builtin)	7.01
Xyce (ADMS)	36.42	Spectre (Verilog-A)	52.61
Xyce (builtin)	26.56	Spectre (builtin)	25.33
https://github.com/arpadbuermen/OpenVAF-reloaded
Source: https://openvaf.semimod.de/docs/details/performance/

---
Xschem schematic editor integration

---
Benchmark results 1/3
RC with pulsed excitation
Graetz rectifier with RC load
Voltage multiplier (diode ladder)
9-stage ring oscillator (PSP103.4)
Evals … number of circuit evaluations

---
Benchmark results 2/3
C6288: 16x16 digital multiplier
Compute 0xFFFF x 0xFFFF
PSP103.4 MOSFETs
10112 transistors, 25380 unknowns
https://codeberg.org/arpadbuermen/VACASK/src/branch/main/...
...benchmark/c6288/vacask/runme.sim

---
Benchmark results 3/3
Default VACASK settings
Modified VACASK settings
Residual tolerance checks enabled
Continuation bypass enabled
Effect of residual tolerance checks (rtc)
No rtc == precision of SPICE
Modified VACASK settings
Modified VACASK settings
Residual tolerance checks disabled
Residual tolerance checks disabled
Effect of continuation bypass (cb)
Effect of inactive element bypass (ieb)

---
Harmonic balance - examples
Gilbert cell mixer, 2 tone HB, 3 sidebands
6 MOSFETS (PSP103.4), 3 resistors
Diode AM demodulator, 2 tone HB, 3 sidebands
diode + R + C
50kHz carrier, 1.01kHz signal (incommensurate)
https://codeberg.org/arpadbuermen/VACASK/...
 ...src/branch/main/test/test_hb5.sim
https://codeberg.org/arpadbuermen/VACASK/...
 ...src/branch/main/demo/gilbert/gilbert.sim

---
Builtin, legacy (SPICE3), and modern devices
- Builtins: voltage & current source, linear controlled sources
- Modern devices: Verilog-A, supported through OpenVAF
  BSIMBULK, BSIM-CMG, BSIM-IMG, PSP, HICUM, VBIC, ...
- SPICE3 devices converted into Verilog-A:
  resistor, capacitor, inductor, diode (levels 1 and 3)
  JFET L1-2, MESFET L1, Gummel-Poon BJT,
  MOSFET L 1-3, 6, 9, BSIM3 3.3.0, BSIM4 4.8.3
- TODO: old versions of BSIM3&4, BSIMSOI
- Verilog-A Distiller
  https://codeberg.org/arpadbuermen/VADistiller

---
Roadmap
- Create a FOSS alternative to commercial RF simulators like Spectre and ADS.
- Convert Skywater PDK
- Faster NOISE and XF analyses (adjunct circuit equations)
- Stability analysis (STAB) and S-parameter analysis (SP)
- Transient noise analysis
- Parallel evaluation (OpenMP), parallel linear solver (MUMPS, SUPERLU?)
- Shooting (PSS) & small-signal family (PAC, PXF, PNOISE, PSP, PSTAB)
- Improve harmonic balance, use FFTW library
- Convolutional linear models (defined in frequency domain, i.e. touchstone)

---
Thank you.